//This code is for the arduino project using Shape Memory Polymers

//Include the servo library
#include <Servo.h>

//Create the servo objects for each motor
Servo myservo1;
Servo myservo2;
Servo myservo3;

//Setting some counter variables
boolean mech_deform1 = false;
boolean mech_deform2 = false;
boolean mech_deform3 = false;
boolean unload1 = false;
boolean unload2 = false;
boolean unload3 = false;
boolean lag_cool1 = false;
boolean lag_cool2 = false;
boolean lag_cool3 = false;

//Setting holder variables for the sensor values and the corresponding temperature
int sensor_1 = 0;
int sensor_2 = 0;
int sensor_3 = 0;
float temperature_1 = 0.0;
float temperature_2 = 0.0;
float temperature_3 = 0.0;

//Setting another counter value
int i = 0;
int j = 0;
int k = 0;
float refvolts = 5; //the amount of volts used in the system
float high_temp = 40.0; //the high temperature value
float low_temp = 30.0; //the low temperature value

//Defining the pins for the servos
int servo_pin1 = 6;
int servo_pin2 = 4;
int servo_pin3 = 8;

//Defining the pins for the temperature sensors
int temp_1 = 15;
int temp_2 = 0;
int temp_3 = 7;

//Defining the delay time for each of the motors
int servo1_neg = 900;
int servo1_pos = 900;
int servo2_neg = 900;
int servo2_pos = 900;
int servo3_neg = 850;
int servo3_pos = 825;

//The positive angles for each of the motors
int pos_ang1 = 230;
int pos_ang2 = 230;
int pos_ang3 = 200;

void setup()
{
  //Set the temperature pins to output
  pinMode(temp_1, OUTPUT);
  pinMode(temp_2, OUTPUT);
  pinMode(temp_3, OUTPUT);
  Serial.begin(9600);
}

void loop()
{
  //Reading teh current sensor value from the temperature sensor
  sensor_1=analogRead(temp_1);
  sensor_2=analogRead(temp_2);
  sensor_3=analogRead(temp_3);
  //Calculating the temperature read from the sensor
  temperature_1 = ((sensor_1-200)*refvolts/1024-0.5)*100;
  temperature_2 = (sensor_2*refvolts/1024-0.5)*100;
  temperature_3 = (sensor_3*refvolts/1024-0.5)*100;
  //Debugging statements
  Serial.print("The temperature reading from the sensor is: ");
  Serial.println(temperature_3);
  //Checking to see if the temperature has reached the higher temperature
  if(temperature_1 >= high_temp && mech_deform1 == false){
    k++;
    //If the polymer has been held at the high temperature for a consistent time
    //then mechanically deform the polymer
    if(k==100){
      mech_deform1 = mech_deform_poly(myservo1, servo1_neg, servo_pin1);
      k=1;
    }
  }
  if(temperature_2 >= high_temp && mech_deform2 == false){
    j++;
    if(j==100){
      mech_deform2 = mech_deform_poly(myservo2, servo2_neg, servo_pin2);
      j=1;
    }
  }
  if(temperature_3 >= high_temp && mech_deform3 == false){
    i++;
    //Debugging statements
    //Serial.print("The i counter variable is: ");
    //Serial.println(i);
    if(i==100){
      mech_deform3 = mech_deform_poly(myservo3, servo3_neg, servo_pin3);
      //Serial.print("The mech_deform variable is: ");
      //Serial.print(mech_deform3);
     i=1;
    }
  }
  //Check to see if the polymer has been cooled
  if(temperature_1 <= low_temp && mech_deform1 == true && unload1 == false){
    //Unload the polymer
    unload1 = unload_poly(myservo1, servo1_pos, pos_ang1, servo_pin1);
  }
  if(temperature_2 <= low_temp && mech_deform2 == true && unload2 == false){
    //Unload the polymer
    unload2 = unload_poly(myservo2, servo2_pos, pos_ang2, servo_pin2);
  }
  if(temperature_3 <= low_temp && mech_deform3 == true && unload3 == false){
    //Unload the polymer
    unload3 = unload_poly(myservo3, servo3_pos, pos_ang3, servo_pin3);
  }
  //Check to see if the polymer has been heated again
  if(temperature_3 >= high_temp && mech_deform3 == true && unload3 == true && lag_cool3 == false){
    i++;
    if(i==100){
      //lag_cool3=true;
      mech_deform3 = false;
      unload3 = false;
      i=1;
    }
  }
// //Give the polymer some time to cool off
// if(temperature_3 <= low_temp && lag_cool3 == true){
// i++;
// if(i==300){
// lag_cool3 = false;
// mech_deform3 = false;
// unload3 = false;
// //Debugging code:
// Serial.println("The variables have been reset.");
// i=1;
// }
// }
}

//This subroutine is used to curl the polymer inward
boolean mech_deform_poly(Servo &servo, int time_neg, int servo_pin){
  //Attach the servo pin to the servo object
  servo.attach(servo_pin);
  //Write the position of the servo motor
  servo.write(-270);
  delay(time_neg);
  servo.detach();
  return(true);
}

//This subroutines unloads the polymer
boolean unload_poly(Servo &servo, int time_pos, int pos_ang, int servo_pin){
  //Attach the servo pin to the servo object
  servo.attach(servo_pin);
  //Write the position of the servo motor
  servo.write(pos_ang);
  delay(time_pos);
  servo.detach();
  return(true);
}