//This program is used to calibrate the temperature sensor

//Define the temperature pin
int temp_pin = 0;

//Define some reference values
float refvolts = 5.0;
int sensor;
float temperature = 0.0;

void setup (){
  pinMode(temp_pin, OUTPUT);
  Serial.begin(9600);
}

void loop(){

  //Reading teh current sensor value from the temperature sensor
  sensor=analogRead(temp_pin);

  //Calculating the temperature read from the sensor
  temperature = (sensor*refvolts/1024-0.5)*100;

  Serial.print("The temperature reading from the sensor is: ");
  Serial.println(temperature);
}